## Slide 1
A Method for Registration of 3-D Shapes
Iterative Closest Point ( ICP )
Paper Review
발표자 : 고대걸

## Slide 2
Iterative Closest Point ( ICP ) Contents
Abstract
Introduction & Literature Review
Mathematical Preliminaries
Iterative Closest Point Algorithm
Experimental Results
Conclusion
A Method for Registration of 3-D Shapes

## Slide 3
01
01
ICP ‘s Idea
02
ICP ‘s advantages
Register sensed data from un-fixtured rigid objects with an ideal geometric model prior to shape inspection.
Useful for deciding fundamental issues such as the congruence (shape equivalence) of different geometric representations
Useful for estimating the motion between point sets where the correspondences are not known.
Abstract
Method for the accurate and computationally efficient registration of 3-D shapes
given an adequate set of initial rotations and translations for a particular class of objects with a certain level of "shape complexity,"
one can globally minimize the mean-square distance metric over all six degrees of freedom by testing each initial registration.
A Method for Registration of 3-D Shapes

## Slide 4
Introduction & Literature Review
02
Introduction
01
Main interests
-> Does a segmented region from a range image match a subset of B-spline surfaces?
02
Solutions
  The point-set matching problem without correspondence
  Free-form surface matching problem
  The free-form curve matching problem
03
Considering
  For purposes of simplicity and relevance to inspection applications based on thousands of digitized points,
  the case of unequal uncertainty among points is not considered.
  2. The removal of statistical outliers is considered a preprocessing step
  3. The assumption that a high-accuracy noncontact measurement device does not generate bad data is reasonable
A Method for Registration of 3-D Shapes

## Slide 5
Introduction & Literature Review
02
Main Purpose
A Method for Registration of 3-D Shapes
-3D data in a sensor coordinate system.
-Model shape in model coordinate system.
Goal is to minimize the distance between model shape and data shape.
Optimal rotation or translation that aligns model shape and data shape.

## Slide 6
02
Introduction & Literature Review
Literature Review
01
02
03
04
05
This work popularized the use of quaternions for least squares registration of corresponding 3-D point sets
Limitation : It relied on the probable existence of reasonably large planar regions within a free-form shape
Developed a solution to the free-form space curve matching problem without feature extraction
Limitation : It has difficulty with very noisy curves
Solve 3-D point-set pose estimation problem using robust methods combined with the least squares SVD registration approach
developed the extended Gaussian image (EGI) methods
work in the area of implicit algebraic nonplanar 3-D estimation with applications to position estimation without feature extraction.
Limitation : Unclear that the effectiveness generalizes well to more complicated surfaces, such as terrain data or a human face.
A Method for Registration of 3-D Shapes

## Slide 7
Mathematical Preliminaries
03
Parametric entity and entity set
Objective function and Newton’s formula
A. Point to Parametric Entity Distance
Implicit entity and entity set
Objective function and formula using Lagrange
B. Point to Implicit Entity Distance
A Method for Registration of 3-D Shapes

## Slide 8
Mathematical Preliminaries
03
Quaternion
C. Quaternion
Objective function and Rotation matrix
C-1. Objective function and Rotation matrix
A Method for Registration of 3-D Shapes

## Slide 9
Mechanism of the ICP
Iterative Closest Point Algorithm
04
A Method for Registration of 3-D Shapes

## Slide 10
Compute the closest points
Registration
01
02
03
04
Mechanism of the ICP
Iterative Closest Point Algorithm
04
Compute the registration
Apply the registration
Terminate the iteration
A Method for Registration of 3-D Shapes
Convergence Theorem

## Slide 11
Accelerated ICP Algorithm
Iterative Closest Point Algorithm
04
A Method for Registration of 3-D Shapes

## Slide 12
Point Set Matching
Experimental Results
04
A Method for Registration of 3-D Shapes
Curve Matching

## Slide 13
Surface Matching
Experimental Results
04
A Method for Registration of 3-D Shapes

## Slide 14
Surface Matching
Experimental Results
04
A Method for Registration of 3-D Shapes

## Slide 15
Conclusion
05
Advantages
01
Disadvantage
02
Ignore
Generalization
Cost
Limitation
03
Unique Value
Time
Same
SLAM?
A Method for Registration of 3-D Shapes

## Slide 16
Thank you for listening